PIX IOS Upgrade Instruction

1. Create PIX Boot helper disk.

Do the following to create Boot helper floppy disk.

(You will need a 3.5 formatted floppy diskette).

For UNIX systems, create the disk using the following command

dd bs=18k <bh512.bin> /dev/rfd0

For PC systems, use the rawrite.exe utility

Place the following files in the same folder on laptop computer

(bh52.bin;Rawrite.exe).

Double click Rawrite file to execute the file.

Enter source file name: = bh52.bin

destination drive: = a:

2. Setup TFTP server on your laptop PC

3. Assign IP address for your laptop (172.26.13.2)

4. Store PIX IOS image file (pix523.bin) into TFTP root directory.

5. Use a RJ-45 cross cable for your laptop and PIX connection directly.

6. Before Upgrade PIX IOS, check current PIX activation key and license

use "sh ver" command on PIX firewall.

7. Insert PIX Boot Disk into PIX floppy drive.

8. Power on or boot PIX.

9. Confirm loaded PIX IOS version.

Cisco Secure PIX Firewall Version 5.2(1)

10. Choose "interface 0" for activating PIX FE interface

(this can be 0-5)

pixboothelper> interface 0

current interface is 0

0:  i82557 @ PCI(bus:2 dev:0 irq:11)    ethernet0 100basetx

1:  i82557 @ PCI(bus:2 dev:1 irq:10)    ethernet1 not_init

2:  i82557 @ PCI(bus:2 dev:2 irq:15)    ethernet2 not_init

3:  i82557 @ PCI(bus:2 dev:3 irq: 9)    ethernet3 not_init

4:  i82557 @ PCI(bus:0 dev:14 irq:10)    ethernet4 not_init

5:  i82557 @ PCI(bus:0 dev:15 irq:15)    ethernet5 not_init

pixboothelper>

11. Assign IP address for PIX interface 0

pixboothelper> address 172.26.13.1

address: 172.26.13.1

12. Specify your TFTP server IP address.

pixboothelper> server 172.26.13.2

server 172.26.13.2

13. select IOS image file for downloading

pixboothelper> file pix523.bin

file pix523.bin

14. start tftp session and reboot system

pixboothelper> tftp

tftp pix523.bin@172.26.13.2........

...................................

...................................

...................................

...............…………......

Received 2138112 bytes.

Flash version 5.0(3), Install version 5.2(3)

Installing to flash

Serial Number: 18036174 (0x11335ce)

Activation Key: 69df99d3 e74f95e0 dce97115 77f9f31a

Do you want to enter a new activation key? [n]n

Writing 2035768 bytes image into flash...

Ready to reboot, please remove the disk.

Rebooting....

15. Confirm PIX IOS version, PIX activation key, license, configuration, and failover status after boot.